PICO-500
- Most detailed information here
- Exposure: 1.27 * 10^5 kg days
  - 250l fiducial volume, filled with C3F8 (density: 1.39 kg/l)
  - Only fluorine is relevant: correction factor 0.81
- 2 bins: 3.2–10keV, 10–50keV
- First bin
  - Use same acceptance as PICO-2L and PICO-60
  - Reduced exposure equivalent to 50% acceptance
- Background: 3, 0.85 events

---
DarkSide-20k
- https://arxiv.org/pdf/1707.08145.pdf
- Exposure: 3.65 * 10^7 kg days
- Threshold: 30 keV (threshold function given, use f200)
- Resolution (crude estimate): 0.05 + (2 keV / Enr)
- 10 bins: 30→80
- Backgrounds
  - Assume 0.4 events from instrumental backgrounds, uniformly distributed
  - Neutrino scattering background: 1.6 events (non-trivial energy dependence)
  - [0.077, 0.117, 0.149, 0.156, 0.149, 0.138, 0.128, 0.119, 0.111, 0.102]

---
LZ
- https://arxiv.org/pdf/1712.04793.pdf
- https://arxiv.org/pdf/1509.02910.pdf
- Exposure: 5.6 * 10^6 kg days
- Resolution: 0.065 + 0.24 / sqrt(Enr / keV)
- 50% acceptance above threshold
- 6 bins: 6→30 keV
- Background: 0.394 events / bin

---
DARWIN
- https://arxiv.org/pdf/1506.08309.pdf
- 200 t yr = 7.3 * 10^7 kg days (30% acceptance)
- Energy window: 5-20 keV (5 bins with 3 keV)
- 99.98% ER rejection → no ER backgrounds
- Resolution: 0.05 + (0.05 keV / E_R)
- Neutrino scattering background: [0.83,0.41,0.29,0.24,0.19] events