PICO-500
- Most detailed information here
- 250l fiducial volume
- Filled with C3F8 (density: 1.39 kg/l)
- Only fluorine is relevant: correction factor 0.81
- Exposure: 1.27 * 10^5 kg days
- 2 bins: 3.2–10keV, 10–50keV
- 50% acceptance for first bin
- Background: 3, 0.85 events

---
DarkSide-20k
- https://arxiv.org/pdf/1707.08145.pdf
- Exposure: 3.65 * 10^7 kg days
- Threshold: 30 keV (threshold function given)
- Resolution (crude estimate): 0.05 + (2 keV / Enr)
- 10 bins: 30→80

---
LZ
- https://arxiv.org/pdf/1712.04793.pdf
- https://arxiv.org/pdf/1509.02910.pdf
- Exposure: 5.6 * 10^6 kg days
- Resolution: 0.065 + 0.24 / sqrt(Enr / keV)
- 50% acceptance above threshold
- 6 bins: 6→30 keV
- Background: 0.394 events / bin